## Slide 1: BIAC MRI Safety Refresher Course
MRI Safety Week – 7/26/2017

## Slide 2: Agenda
Basics of MR Safety
  15 minute video from Dr. Frank Shellock
  Dangers of MRI
MR Safety and Subject Care in Practice
  Pre-scan Screening
  Day of Scan Procedure
  Adverse Event Reporting
  Data Quality & Movement
Future Announcements from BIAC

## Slide 4: Dangers of MRI
Consequence of bringing ferromagnetic objects in the scanning room
    Projectile: https://www.youtube.com/watch?v=plvIEf7JsKo
Consequence of allowing subjects with non-ferromagnetic but electrically conductive material into the scanner
    Tissue heating or burn (caused by material acting as a looped RF antenna): https://www.youtube.com/watch?v=4t-qRAyoh-I
    Not limited to patches: other objects include but are not limited to gold jewelry, certain types of makeup/mascara, electrically conductive implants

## Slide 5: Pre-Scan Screening
All subjects must be either phone screened or interviewed for MRI safety in person before being scheduled for a scan
  Highly recommended to administer official BIAC MRI Safety Screening Form
Any questions or concerns about MRI safety found in the initial screening should be addressed with Todd and the MRI Technicians at least 48 hours before the scan
  Protocol dependent: based on clinical benefit over risk, some protocols may be IRB approved to scan with certain implants when compared to others

## Slide 6: Pre-Scan Screening
MRI Technicians typically are meeting subjects for the first time the day of the scan and are a last line of defense
  Responsibility to determine initial MRI safety and subject quality is up to individual lab faculty and staff
  Emphasize importance of MRI Safety to subject during thorough review of medical history
    May require obtaining medical record authorization to review make and model of any implanted metal or part of medical history
    Emphasis on reviewing and researching any past surgeries as many subjects may not know they have implanted metal after certain procedures (i.e. wire sutures or a screw/pin)
    Even if implants are deemed safe for scanning, they may cause artifacts

## Slide 7: Examples of Pre-Screening Resources
Example of IRB Approved Phone Screening
BIAC MRI Safety Screening
Dr. Frank Shellock’s MRI contraindication database (use in consult with BIAC) - http://www.mrisafety.com

## Slide 8: Day of Scan Procedure
Step 1: Escort subject to MRI hallway and ask them to place all belongings into lockers
Step 2: Ask subject to remove all metal objects from their person and place in locker (jewelry, bobby pins, credit cards, loose change, etc)
Step 3: Ask subject to pat and empty any and all pockets
Step 4: Have subject fill out BIAC MRI Safety Sheet and review for any last minute changes in MRI safety since the pre-screen
All subjects should be MRI ready before entering the console room

## Slide 9: Day of Scan Procedure – cont’d
Step 5: If scanning a woman of child bearing potential, conduct the urine pregnancy test
Step 6: Ask subject to re-check for any metal on their person or in their pockets
Step 7: Subject will be wanded to ensure there is no metal
Step 8 : MRI Tech will review BIAC MRI Safety Sheet and begin their scanning procedure

## Slide 10: Adverse Event Reporting
Adverse event: an accident, injury, illness, or other health complaint raised by a subject as an apparent or potential consequence of his or her participation in a research study
  Injury by a projectile, interruption of the functioning of a medical device such as a pacemaker or neurostimulator, burns, persistent complaints about dizziness, ringing in the ears, or pain
  An accident that does not result in injury but that exposed the subject to potential harm should also be considered an adverse event (a projectile that just misses hitting a subject and causes fear or anxiety in the subject)

## Slide 11: Adverse Event Reporting
If medical attention is needed, immediately alert emergency room
Once the subject is safe, report to Dr. Allen Song and Dr. Todd Harshbarger
Report to the IRB within 10 days of occurrence
Report to Duke’s Office of Risk Management for advice with subject relations
Gray areas can exist between a subject complaint and an adverse event
  Use best judgment
  Err on side of full disclosure

## Slide 12: Data Quality and Movement
When screening subjects before the MRI, incorporating a mock scan can help identify if subjects will be able to remain still for the duration of the scan
Be observant of medical conditions that may cause greater than normal movement (ex. Bronchitis in the winter months, a common cold, or a movement disorder)
Experimenters at the scanner should be observing data acquisition and noting if there are any artifacts
  If subject movement – remind subject to be still, or if it continues, end scan early to save money by paying a cancellation fee for the time not used
  If artifact from MRI – immediately submit a trouble ticket for review from BIAC Help

## Slide 13: Data Quality and Movement
Utilize free UserTest sessions on calendar to run through protocol multiple times before beginning data collection
Consult with BIAC to ensure scanning protocol is correct before booking scanner time
Data should be reviewed for QA as soon as possible after collection
Utilize the online trouble ticket system to alert BIAC to potential issues with scanning or reach out to Dr. Todd Harshbarger
    If using a BIAC Volunteer subject, alert Catherine as well
    BIAC is not responsible for artifacts related to subject motion

## Slide 14: Data Quality Resources
BIAC Services: https://www.biac.duke.edu/services/
  Automatic QA Reports for each scan and Trouble Ticket System within Exam Tracker

## Slide 15: Future Announcements
Updated Level 1 orientation/training for new faculty and staff
Updated Standard Operating Procedures
BIAC User Manual on wiki to reflect updated SoPs
Be on the lookout in the coming months for an announcement once these materials are released

## Slide 16: Summary
Subject MRI safety is a two-way street and we hope to continue to foster the lines of communication about MRI Safety with all BIAC users
Remain vigilant with screening for MRI Safety at all points during the course of data collection
In addition to the upcoming release of the new Level 1 Safety Training, we ask that you instill dedication to subject MRI safety for all new incoming members of your lab
A copy of this presentation and described resources can be found under the “Education” section on the BIAC Wiki at https://wiki.biac.duke.edu/biac:mrisafetyrefresher